## Slide 1: eAP: A Scalable and Efficient In-Memory Accelerator for Automata Processing
By Lane Arnold, Assiya Kalykova, Edward Auttonberry

## Slide 2: What is the importance of Finite Automata in the real world?
In the world of pattern matching: network security, data mining, genomics
All the patters are complex, needing to support a variety of inexact matches.
On leading methodology to solve these inexact pattern matching is regular expression or equivalent Finite Automata.
The demand of accelerated pattern matching has motivated many recent studies to utilize Automata processing hardware accelerators for deep packet inspection, natural language processing, pattern mining, and machine learning.
Without a doubt, Finite Automata are important to the real world.

## Slide 3: Why our current technologies don’t cut it
Nature of CPUs and GPUs:
Performance growth in CPU’s are slowing down
FA processing on CPUs and GPUs:
  Exhibit irregular memory access patterns
  This then disables prediction and data forwarding techniques and unpredictable memory bandwidth
  Thus we need memory accelerators designed for FA processing!!

## Slide 4: Requirements
A memory accelerator that:
  Is scalable
  Has low power-consumption
  Is efficient
  The eAP designed by Elaheh Sadredini et. al. meets all of these requirements.

## Slide 5: What exactly is eAP?
eAP is a modification of a another in-memory processor called Automata Processor (AP), developed by Micron Technology, Inc.
AP intended to provide a solution for the problems previously posed regarding processing NFAs.

## Slide 6: The Crossbar and the Problem with AP
The Crossbar (CB) is an architecture pattern in rows of memory cells that provides a route of connectivity among all cells in the row.
AP implements a Full Crossbar (FCB) to support NFAs with full interconnectivity, e.g. every state has a transition to every other state. This means that all cells in a row of memory are dedicated to tracking state transitions.
However, benchmarks demonstrate an average utilization of FCB advantages of only 0.53%
This means that AP is highly inefficient for low-interconnectivity NFAs.

## Slide 7: The Solution: Reduced Crossbar
The Reduced Crossbar (RCB) pattern repurposes unused cells in rows of memory for pattern matching against states of an NFA, reducing the effect of the Crossbar
This reduction in accessibility from the crossbar increases the density of memory cells, increasing NFA processing throughput
The RCB modification is still capable of emulating an FCB when needed at a small cost to state matching
RCB and FCB blocks are capable of intercommunication, allowing eAP to utilize the advantages of FCB while leaving the work of state matching to other blocks of memory

## Slide 8: Memory Cell Architecture
Requirements:
  Non-destructive read – the bit value at a location in memory must not be disturbed by a read operation
  Stable parallel read combinations – parallel read operations need to be synchronized when outputting to a common bit-line
These requirements are to support read-time logical OR operations to conduce the efficient representation of many-to-many relationships in NFAs
A 2 Transistor 1 Diode (2T1D) DRAM format meets these requirements and is denser than the other valid options like an 8 Transistor SRAM format