## Slide 1: Biocompatibility Testing
BIEN 235
Dr. Teresa Murray
Louisiana Tech University
College of Engineering and Science

## Slide 2: Membrane of Cells
All cells are bounded by a membrane called plasma membrane, which serves as a dynamic interface between the internal environment of the cell and the external environments.
Cell Structure: http://www.youtube.com/watch?v=PXbv95P3uhI
http://www.youtube.com/watch?v=fNyq4A08mTo
http://espanol.video.yahoo.com/watch/40408/808847
Part II MEDICAL
Chap 16 Cell

## Slide 3: Receptors
On the external surface of the plasma membranes, many of the membrane proteins and lipids are conjugated with short chains of polysaccharide, the combinations called glycoprotein and glycolipids
These glycoprotein and glycolipids are called receptors. They participate in important interactions such as cell adhesion, recognition and response to protein hormones (cell communication).
Part II MEDICAL
Chap 16 Cell

## Slide 4: Nucleus, Cytoplasm, Cytoskeleton
Inside cell membrane, the cell is composed of three basic parts: nucleus,
cytoplasm & cytoskeleton
Both the cytoplasm and nucleus contain a number of sub-cellular elements, called organelles.
Part II MEDICAL
Chap 16 Cell

## Slide 5: Apoptosis vs Necrosis
Either apoptosis or necrosis can be identified morphologically using histological techniques
Part II MEDICAL
Chap 16 Cell

## Slide 6: Phenotype
A phenotype is any observable characteristic (or traits) of an organism (including cells): such as its morphology, development, biochemical or physiological properties, or behavior.
Fibroblasts
Neuron
Red blood cells
Part II MEDICAL
Chap 16 Cell

## Slide 7: Cytoskeleton
Within the cytosol, there is a network of minute tubules and filaments, collectively known as the cytoskeleton, which provides structural support for the cell and its organelles, as well as providing a mechanism for transfer of materials within the cell and movement of the cell itself.
Part II MEDICAL
Chap 16 Cell

## Slide 8: Mitosis
Cell division is also called mitosis.
Video of cell division:
http://www.youtube.com/watch?v=aDAw2Zg4IgE
http://www.youtube.com/watch?v=rgLJrvoX_qo
Part II MEDICAL
Chap 16 Cell

## Slide 9: Cell Growth Curve
Cell proliferation has been observed to occur in three phases, called lag, log and plateau phase.
The doubling time is the period required for a population of cells to double in number.
Part II MEDICAL
Chap 16 Cell
Growth dynamics occurs under controlled growth conditions in vitro, in an excess of nutrients. The lag phase an artefact of the relatively slow recovery of cells from cryostorage. However, similar proliferation dynamics occur in vivo as well.

## Slide 10: Confluency
100 % Confluency
50 - 60 % Confluency
Part II MEDICAL
Chap 16 Cell

## Slide 11
Selection of Stable transfected Cell Lines
a. Picked individual clonal colonies by using cloning disks
b. Placed cloning disk into 6 well plate containing CDMEM with hygro
c. Formation of β2.2.4-nAChRs clonal colonies

## Slide 12
Preliminary tests of biocompatibibilty using cell culture
Louisiana Tech University
College of Engineering and Science
http://www.biology-blog.com/images/
blogs/9-2008/cell-culture-17601.jpg
www.translational-medicine.com/content/figures/1479-5876-3-14-1-l.jpg
Vital red: stains live cells
Trypan blue: stains dead cells
Changes in morphology: vaculoes, blebs, crenation, and rounding are examples.
Temperature, nutrient and pH controlled

## Slide 13
Louisiana Tech University
College of Engineering and Science
Table and description from Ch. 5.2 text: Ratner et al., 2004
Must standardize methods for valid comparisons: number of cells, growth phase of the cells, cell type (generally, use established, well-characterized cell lines), duration of exposure, test sample size (e.g., geometry, density, shape, thickness), and surface area of test sample.
Example: A small increase in size of sample with toxic extractable chemicals could change the effect on cells from mildly toxic to very toxic.

## Slide 14: Receptor-mediated internalization of small molecules (e.g., Ab1-42)
Ab1-42 binds to receptor  when receptor is endocytosed, Ab1-42 enters cell with receptor
Graphics: Teresa A Murray © 2012
Plasma
membrane
nACh receptor
Endosome
Ab1-42
Cytosol
Cytosol
Louisiana Tech University
College of Engineering and Science

## Slide 15: Internalization of toxic small molecules
Louisiana Tech University
College of Engineering and Science
Receptor-medicated internalization of small molecules can be toxic to cells
Cells can die or become unhealthy (poor function, cancer, …)

## Slide 16: Internalization of toxic Aβ1- 42 peptide
Louisiana Tech University
College of Engineering and Science
Receptor-medicated internalization of small molecules, such as Aβ1-42
Amyglo stains oligomeric Aβ1-42 by exhibiting blue fluorescence (see image)
Source: www.biosensis.com
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 17: Amylo-Glo staining of Aβ1- 42
Incubation with 0.1 % Amylo-Glo staining solution in 0.9%saline
Staining
Washing
Incubate cells with 4% paraformaldehyde (cross links proteins)
Rinse 3 times with phosphate buffered saline
Imaging
3D images of live cells by multiphoton microscopy
Compare levels of internalization using relative intensity of staining
Fixation
Analysis
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 18
a7β2 nAChRs
SHEP 1 cells
Amylo-Glo staining with and without Aβ1- 42
Scale bar 20 mm for all images
With
Without
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 19: Assessing internalization of Aβ1-42
SH-EP1 cells with … | Normalized intensity of cells incubated with Aβ1-42
No receptors | 1.00
a7β2 nACh receptors | 2.90
a7 nACh receptors | 4.49
A region of interest was drawn around each cell, excluding the nucleus, using Image J software.
Mean fluorescence intensity for cells incubated with Aβ1-42 were normalized to (divided by) the intensity of cells with no Aβ1-42 incubation.
SH-EP1 cells were the negative control condition and cells expressing the a7-nACh receptor were the positive control condition.
a7β2-nAChRs
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 20
Incubate cells with Aβ1-42
Incubation
4, 12, 24, 48, 96 hour
Incubation
Periods
Method
Trypan blue to stain dead cells
Determination Of Cell Death Rate
Imaging
Olympus DP71 color camera and a 20X objective lens
Image source: http://braukaiser.com/blog/wp-content/uploads/2013/04/fermentation_experiment_o2_access_B.jpg
Notes: From Himgauri V. Naik’s Master’s Thesis 2014

## Slide 21: Images SH-EP1 cells with α7β2-nACh Receptors
Without oligomeric Aβ1-42 peptide
With oligomeric Aβ1-42 peptide
Confluent | 24 hrs | 48 hrs | 96 hrs | 96 hr tryphan blue
Scale bar 20 mm
Same for all images
Notes: α7β2.2.4-nAChR expressing SH-EP1 cells (Adapted from Himgauri V. Naik’s Master’s Thesis 2014)

## Slide 22
Images of negative control SH-EP1 cells
Confluent | 24 hrs | 48 hrs | 96 hrs | 96 hr trypan blue
Without oligomeric Aβ1-42 peptide
With oligomeric Aβ1-42 peptide
SH-EP1 cells do not have nicotinic receptors.
These are used for the negative control condition.
Scale bar 20 mm
Same for all images
Notes: SH-EP1 cells (Adapted from Himgauri V. Naik’s Master’s Thesis 2014)

## Slide 23: Cell-based assays using fluorescence
  Changes in protein expression (ma7-YFP protein) in SH-EP1 cells
Plasma Membrane
Graphics: Teresa Murray 2007; plot: Murray, unpublished 2008
Molecular Devices, 2008
FP-labeled proteins

## Slide 24: In vivo testing
Louisiana Tech University
College of Engineering and Science
g
h
Source: Lee, Murray, et al. 2016
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 25: In vivo testing
Louisiana Tech University
College of Engineering and Science
g
Source: Lee, Murray, et al. 2016
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 26: In vivo testing
Louisiana Tech University
College of Engineering and Science
g
h
Source: Lee, Murray, et al. 2016
Notes: Adapted from Himgauri V. Naik’s Master’s Thesis 2014

## Slide 27: Oxidized dextran S.A.M. on electrodes
Antibody stain colors are:
Astrocytes Neurons
T Murray 2002, unpublished
Murray, T.A., et al., REAS 2003
No cells adhered to electrode surface
Cells (stained purple) adhered to electrode surface
Extensive encapsulation and inflammation (red stain), few neurons (blue stain)
Poor signal to noise ratio, likely due to encapsulation and exclusion of neurons
Thin capsule, more neurons
Good S:N likely due to larger numbers of neurons
No S.A.M.
S.A.M.
T Murray 2002, unpublished
Murray, T.A., et al., REAS 2003
Notes: Steve(?): You can get this directly from paper’s conclusions.

## Slide 28: PI & Fluorescent Nissl Stain
Nissl stain
Propidium iodide
Colocalized (white)
Dyes used to show neurons (green) and damaged cells (red)
after removal of GRIN lens
Murray, 2010, unpublished
Notes: 20110108_PI_Nissl_Implant_2_5a_350um_830nm_3X_065_YFP_1Ch_green
20110108_PI_Nissl_Implant_2_5a_350um_770nm_3X_066_PI_1Ch_red
20110108_PI_Nissl_Implant_2_5a_350um_3X_065_066_1Ch_RGW
Propidium Iodide Stain http://en.wikipedia.org/wiki/Propidium_iodide Propidium iodide (or PI) is an intercalating agent and a fluorescent molecule with a molecular mass of 668.4 Da that can be used to stain DNA. When excited with 488 nm wavelength light, it fluoresces red and can be detected with 562-588 nm band pass filter. Propidium iodide is used as a DNA stain for both flow cytometry to evaluate cell viability or DNA content in cell cycle analysis [1] and microscopy to visualise the nucleus and other DNA containing organelles. It can be used to differentiate necrotic, apoptotic and normal cells.[2] Propidium Iodide is the most commonly used dye to quantitatively assess DNA content. [3][citation needed] Propidium iodide (PI) binds to DNA by intercalating between the bases with little or no sequence preference and with a stoichiometry of one dye per 4–5 base pairs of DNA. PI also binds to RNA, necessitating treatment with nucleases to distinguish between RNA and DNA staining.[4] Once the dye is bound to nucleic acids, its fluorescence is enhanced 20- to 30-fold, the fluorescence excitation maximum is shifted ~30–40 nm to the red and the fluorescence emission maximum is shifted ~15 nm to the blue. Although its molar absorptivity (extinction coefficient) is relatively low, PI exhibits a sufficiently large Stokes shift to allow simultaneous detection of nuclear DNA and fluorescein-labeled antibodies, provided the proper optical filters are used. PI is suitable for fluorescence microscopy, confocal laser scanning microscopy, flow cytometry, and fluorometry. PI is membrane impermeant and generally excluded from viable cells. PI is commonly used for identifying dead cells in a population and as a counterstain in multicolor fluorescent techniques.[5]

## Slide 29: Track of implanted EEG electrode
NeuroNEM Epilepsy Project: Unpublished, K. Ponder, 2017. Scale bar is 100 mm.
Fixed brain tissue
Paraffin embedded
H&E stain
Little disruption of surrounding tissue

## Slide 30
Louisiana Tech University
College of Engineering and Science
Table from text: Ratner et al., 2004
You do not need to memorize the entire table, but know the three assessments highlighted in yellow.

## Slide 31
Louisiana Tech University
College of Engineering and Science

## Slide 32: Systemic Toxicity and Hypersensitivity
Physical breakdown of biomaterials
  encapsulation of debris
  transport to & build-up in liver and other organs
Toxicity from leached compounds
  concentration [mg/kg]
  compound- & tissue-dependent
  length of exposure
Immunotoxicity and hypersensitivity
  allergy (unpredictable)
  intolerance – inherited sensitivity
Louisiana Tech University
College of Engineering and Science

## Slide 33
Louisiana Tech University
College of Engineering and Science
Tables from text: Ratner et al., 2004
increases immune-system responses to chemicals
local tissue inflammation response to chemicals
changes in DNA
local structure/function

## Slide 34
Louisiana Tech University
College of Engineering and Science
Tables from text: Ratner et al., 2004

## Slide 35
Louisiana Tech University
College of Engineering and Science
Tables from text: Ratner et al., 2004
Some test standards useful for testing biomaterials
(This is not a complete list)
Know that ISO 10,993-# standards are for biocompatibility tests
c

## Slide 36
Louisiana Tech University
College of Engineering and Science
The following slides contain prices for preclinical testing by a commercial laboratory. They perform tests on materials that will be used in applications to the FDA for premarket approval.
You only need to memorize information that is highlighted in yellow on the following tables of tests.

## Slide 37
2010 Price List for Biocompatibility Testing
Actual price list from a testing laboratory with the company’s name redacted
Louisiana Tech University
College of Engineering and Science
Cytotoxicity – ISO 10993-5, USP <87> |  | 
Test Description | Test Code | Price
Agar Overlay cell culture assay |  | 
24 hours incubation, triplicate, L929 cells | CTX101 | $135.00
MEM Elution cell culture assay |  | 
MEM elution, 48 hours incubation, triplicate, L929 cells, 24 hr. extraction | CTX110 | $135.00
MEM elution, 72 hours incubation, triplicate, L929 cells, 24 hr. extraction | CTX115 | $135.00
MEM elution, titration, 4 dose levels, L929 cells | CTX125 | $290.00
MEM elution, Japan MHLW | CTX210 | Quote
MEM elution or Agar overlay, additional reads |  | 
Each study/set | CTX701 | $25.00
The next slides list many of the common tests used for preclinical studies of medical devices. Numerous tests relate to biomaterials. Not all are used for a particular device. Note, several of the tests cite a particular published standard for testing.

## Slide 38
Raw Materials Characterization ISO 10993-12; ISO 10993-18 |  | 
Test Description | Test Code | Price
Differential Scanning Calorimetry (DSC) |  | 
Sample preparation and analysis, each | DSC101 | $160.00
Fourier Transform Infrared Analysis (FTIR) | IRX110 | 
FTIR sample analysis, each |  | $110.00
Sample preparation (extraction or KBr press), each |  | $35.00
Library search, each |  | $35.00
Physicochemical test, USP plastics USP <661> |  | 
If the nonvolatile residue is <5 mg then the residue on ignition is not required, per USP |  | 
Complete | PCT101 | $450.00
Includes water extraction, buffering capacity, heavy metals, nonvolatile residue, residue on ignition |  | 
Complete, without residue on ignition | PCT105 | $375.00
Includes water extraction, buffering capacity, heavy metals, nonvolatile residue |  | 
Extractable/Leachable Analytical Chemistry |  | 
ICP-MS, Full scan | CHX110 | Quote
GC-MS for Volatile organic compounds | CHX110 | Quote
GC-MS for Semi-volatile organic compounds | CHX110 | Quote
LC-MS for Non-volatile organic compounds | CHX110 | Quote
Louisiana Tech University
College of Engineering and Science

## Slide 39
Toxicology & Biocompatibility (in vivo)– ISO 10993
Sensitization
Maximization (ISO)
Local Lymph Node Assay
Buehler Method
Maximization (Japan MHLW)
Irritation
Intracutaneous Reactivity (ISO)
Intracutaneous Toxicity (USP)
Primary Eye Irritation
Primary Skin (ISO)
Bladder Irritation
Vaginal/Mucosal Irritation
Intracutaneous Injection (Japan MHLW)
FHSA Skin Irritation
Systemic Toxicity
Systemic Injection
Material Mediated Pyrogen
Sub-Chronic Toxicity: Intravenous Toxicity with Histopathology
Sub-Chronic Toxicity: Intraperitoneal Toxicity with Histopathology
Implantation (ISO): 7, 14, 30, 60, or 90 days
USP Class III, complete: Includes intracutaneous irritation and systemic toxicity
USP Class VI, complete: Includes intracutaneous irritation, systemic toxicity, and 7 day implant
All of the prices for these tests are quoted
Louisiana Tech University
College of Engineering and Science

## Slide 40
Genotoxicity – ISO 10993-3 |  | 
Test Description | Test Code | Price
Ames Mutagenicity Tests, OECD 471, ICH S2A and S2B |  | 
Ames test: Solids |  | 
2 extracts, 5 strains, plate incorporation (Saline and DMSO) | GTX110 | $2,545.00
Ames test: Solids |  | 
5 strains, plate incorporation, one extract | GTX130 | $1,855.00
Ames test: Soluble chemicals |  | 
5 strains, 1 dose, plate incorporation | GTX140 | $1,855.00
5 strains, 5 doses, plate incorporation | GTX145 | $3,975.00
Ames test: Base Oils, ASTM E1687-98 |  | 
Pre-incubation, 1 strain | GTX150 | $795.00
Chromosomal Aberration, OECD 473 (solid sample/device extraction) |  | 
Test utilizing CHO cells 1 extract | GTX210 | $9,010.00
Test utilizing CHO cells, 2 extracts | GTX220 | $12,720.00
Louisiana Tech University
College of Engineering and Science
c